RESOURCE AREA:

1. Doorways/Throughways

- Entryway area 30” x 48”

2) Door width at 32” minimum

- Threshold ½”

4) Door-weight to open less than 5 lbs.

- Door control hardware---lever

- Hardware @ 48” height from floor

- Throughways/aisles are least 36” in

continuous width (ADAAG 4.3.3)

2. Furniture: Tables / Counters/ Desks/Cubicles/Chairs –

- Clear Floor Space Seating

@ 30” by 48”; 60”x60” ideal

- Knee Space @ 19” deep x 30” wide x

27” table skirt to floor

(of the 30” by 48” under table)

3) Surface Top to Floor @ 28” –34”

- Adjustable features to Table: Tray for Keyboard and

Trackball Mouse relative to Desk Surface

- Mounted at the 27” min. table skirt to floor height

- Tray is adjustable at 27” high (adult)  – 15” Low (children)

- Tray tilting adjustability

- Wide enough for  keyboard and trackball mouse

- Distance from Keyboard to Monitor at 30”

- Ergo Chairs with Adjustable Arm Rests to Table /Desk Surface

- Aisles between tables @ 36” width

(clearance around desks)

8) No Protrusions

3. Floor Surface/Slopes/Levels

1) Surface is stable and firm

2) Floor  is level

3) Carpet is securely attached?

4.  Signage

1) Directional Signs

- Room/Facility Identification

60” height; adjacent latch side of door;

Braille and Raised Lettering/Figures

- Raised lettering / Braille Eq. Labels

5. Pamphlet / Materials Displays—Book Shelves

- There is a 30” x 48” clear floor space in

front of display / bookshelves (ADAAG 4.25.2)

- Side reach to shelves @ 9”-58” from floor

or

- Front reach to shelves @ 15”-48” from floor

(ADAAG 4.25.3)

6. Controls relative to Desks/Cubicles/Tables

- Heights between 9”-54” from the floor  on

parallel approach

- Heights between 15”-48” from the floor  on

frontal approach

NOTES: